## Slide 1: Analysis of peering strategy adoption by transit providers in the Internet
Aemen Lodhi (Georgia Tech)
Amogh Dhamdhere (CAIDA)
Constantine Dovrolis (Georgia Tech)
2nd Workshop on Internet Economics (WIE’11)

## Slide 2: Outline
Motivation
Objective
The model: GENESIS
Results
  Adoption of peering strategies
  Impact on economic fitness
  Who loses? Who gains?
Alternatives
Conclusion

## Slide 3: Motivation
Peering strategies of ASes in the Internet
(source: PeeringDB www.peeringdb.com)

## Slide 4: Motivation
Peering policies for networks classified by traffic ratio (source: PeeringDB www.peeringdb.com)

## Slide 5: Objective
Why do transit providers peer Openly?
Impact on their economic fitness?
Which transit providers lose/gain?
Are their any alternative peering strategies?
Enterprise customer
Transit Provider
Transit Provider
Internet
Enterprise customer
Content Provider
Content Provider

## Slide 6: Approach
Agent based computational modeling
Scenarios
Conservative
Selective
Restrictive
Non-conservative
Selective
Restrictive
Open
vs.

## Slide 7: The model: GENESIS*
Agent based interdomain network formation model
Incorporates
  Co-location constraints in provider/peer selection
  Traffic matrix
  Public & Private peering
  Set of peering strategies
  Peering costs, Transit costs, Transit revenue

## Slide 8: The model: GENESIS*
  Fitness = Transit Revenue – Transit Cost – Peering cost
Objective: Maximize economic fitness
Optimize connectivity through peer and transit provider selection
Choose the peering strategy that maximizes fitness

## Slide 9: Peering strategies
Restrictive: Peer only to avoid network partitioning
Selective: Peer with ASes of similar size
Open: Every co-located AS except customers

## Slide 10: results

## Slide 11: Strategy adoption by transit providers
Chart: Scenarios
| Conservative | Non-conservative
Restrictive | 10 | 2
Selective | 90 | 28
Open | 0 | 70

## Slide 12: Why do transit providers adopt Open peering?
x
y
z
w
v
Save transit costs
But your customers are doing the same!
Affects:
Transit Cost
Transit Revenue
Peering Cost

## Slide 13: Why gravitate towards Open peering?
x
y
z
w
z w,
z y,
traffic bypasses x
x lost transit revenue
Options for x?
x regains lost transit revenue partially
Y peering openly
x adopts Open peering
Not isolated decisions
Network effects !!
z w,
traffic passes through x

## Slide 14: Impact on fitness of transit providers switching from Selective to Open
70% providers have their fitness reduced

## Slide 15: Fitness components: transit cost, transit revenue, peering cost?
Reduction in transit cost accompanied by loss of transit revenue

## Slide 16: Fitness components: transit cost, transit revenue, peering cost?
Significant increase in peering costs
Interplay between transit & peering cost, transit revenue

## Slide 17: Avoid fitness loss?
x
y
z
w
x
y
z
w
vs.
Lack of coordination
No incentive to unilaterally withdraw from peering with peer’s customer
Sub-optimal equilibrium

## Slide 18: Which transit providers gain through Open peering? Which lose?
Classification of transit providers
  Traffic volume
  Customer cone size
Chart: Strategy adoption by different classes of transit providers
| Small Traffic Small Customers | Small Traffic Large Customers | Large Traffic Small Customers | Large Traffic Large Customers
Selective | 11.4793 | 16.4609 | 40.317 | 46.4589
Open | 85.3254 | 82.3045 | 59.1316 | 53.2578
Restrictive | 0.55134 | 0.28329 | 1.2346 | 3.1953

## Slide 19: Who loses? Who gains?
Who gains: Small customer cone small traffic volume
  Cannot peer with large providers using Selective
  Little transit revenue loss
Who loses: Large customer cone large traffic volume
  Can peer with large transit providers with Selective
  Customers peer extensively

## Slide 20: Alternatives: Open peering variants
Do not peer with immediate customers of peer (NPIC)
Do not peer with any AS in the customer tree of peer (NPCT)
x
y
z
w
NPIC
x
y
z
w
v
NPCT

## Slide 21: Fitness analysis Open peering variants
Collective fitness with NPIC approaches Selective

## Slide 22
47% transit providers loose fitness compared to Conservative scheme with Selective strategy
Fitness analysis Open peering variants
OpenNPIC vs. Selective
OpenNPIC vs. Open

## Slide 23
Why the improvement?
  No traffic “stealing” by peers
  Aggregation of peering traffic over fewer links (economies of scale !!)
  Less pressure to adopt Open peering
Why did collective fitness not increase?
  Non-peer transit providers peer openly with stub customers
Fitness analysis Open peering variants

## Slide 24
Why NPIC gives better results than NPCT?
  Valley-free routing
  x has to rely on
  provider to reach v
Fitness analysis Open peering variants
24
x
y
z
w
v
NPCT

## Slide 25
Gravitation towards Open peering is a network effect for transit providers
Extensive Open peering by transit providers in the network results in collective loss
Coordination required to mitigate
No-peer-immediate-customer can yield results closer to Selective strategy
Conclusion

## Slide 26: Thank you

## Slide 27: Motivation
Traffic ratio requirement for peering?
(source: PeeringDB www.peeringdb.com)

## Slide 28: Introduction
Enterprise customer
Transit Provider
Transit Provider
Internet
Enterprise customer
Content Provider
Content Provider

## Slide 29: Traffic components
Traffic consumed in the AS
Transit traffic = Inbound traffic – Consumed traffic
same as
Transit traffic = Outbound traffic – Generated traffic
Autonomous system
Inbound traffic
Traffic transiting through the AS
Traffic generated within the AS
Outbound traffic

## Slide 30: Customer-Provider traffic comparison – PeeringDB.com
Traffic carried by the AS

## Slide 31: Customer-Provider traffic comparison
2500 customer-provider pairs
90% pairs: Customer traffic significantly less than provider traffic
9.5% pairs: Customer traffic larger than provider traffic (difference less than 20%)
0.05% pairs: Customer traffic significantly larger than provider traffic

## Slide 32: Geographic presence & constraints
Link formation across geography not possible
Regions corresponding to unique IXPs
Peering link at top tier possible across regions
Geographic overlap

## Slide 33: Logical Connectivity

## Slide 34: Traffic
Traffic for ‘N’’ size network represented through an N * N matrix
Illustration of traffic matrix for a 4 AS network
Consumed traffic
Generated traffic
Traffic sent by AS 0 to other ASes in the network
Traffic received by AS 0 from other ASes in the network
Intra-domain traffic not captured in the model

## Slide 35: Peering strategy adoption
Strategy update in each round
Enumerate over all available strategies
Use netflow to “compute” the fitness with each strategy
Choose the one which gives maximum fitness

## Slide 36: Peering strategy adoption
No coordination
Limited foresight
Eventual fitness can be different
Stubs always use Open peering strategy
Time
1
2
3
Restrictive
Selective
Open
Restrictive
Selective
Open
Restrictive
Selective
Open
Open
Selective
Open