NCAP
Paul Vixie, ISC
with
Duane Wessels, Measurement Factory
July, 2007

---
PCAP Pros and Cons
PCAP works at the packet (interface) level
  - lots of useless link-level drivel in *.pcap files
  - every PCAP application has a big switch()
  - new link formats are not backward compatible
Impedance mismatch w/ WAN analysis:
  - need IP (UDP) reassembly of large EDNS
  - need TCP reassembly (ordering, duplicates)

---
IP (UDP) Reassembly
Challenges:
  - IP fragments only include UDP headers in first fragment
  - each user-mode reassembler has to ask BPF for all frags and then do flow isolation
Dangers:
  - bad guys wanting to evade trivial analysis and detection can force large-EDNS
  - all known existing tools won't reassemble IP

---
TCP Reassembly
Challenges:
  - TCP segments can arrive out of order and/or be duplicated
Dangers:
  - any transaction that falls back to TCP will probably be missed by all existing analysis tools

---
PCAP File Format Problems
Link level information
  - When analyzing WAN data, the link level information is almost never interesting
  - Most PCAP analyzers skip it altogether
  - When combining PCAP streams, a unified output linktype has to be chosen
Packet size problems
  - snaplen and packet size are 16-bit fields
  - DNS message length is also 16 bits
  - DNS+UDP+IP can be larger than 16 bits

---
NCAP File Format Proposal
Universal format, no interface-specific data
  - All fields are 32-bit network byte order
  - Original wire-format headers (IP, UDP, TCP, etc) are simply discarded
Enumerations
  - network: IP, IP6
  - transport: UDP, TCP
Payloads
  - UDP: sport, dport, length, payload
  - TCP: sport, dport, length, offset, payload

---
NCAP Library Proposal
libncap would appear similar to libpcap
  - some evolution, fewer rough edges in the API
libncap would probably be implemented using libpcap
  - pass the filters across to the kernel
  - grab the output from the kernel
  - reassemble packets/segments, strip headers
  - make and deliver ncap-format messages
Challenges:
  - event handling is still nonportable, so merging input from many interfaces will be tricky

---
NCAP Kernel Module Proposal
The kernel already has efficient packet and segment reassemblers
An NCAP kernel module to tap into data as it passes into/outof the transport would be more efficient than doing it in user mode
This would only work for locally sourced and locally destined traffic
Use of the kernel module would be optional, and hidden behind the NCAP library API
Not very compelling at the moment

---
Implications on Passive DNS
For OARC passive DNS, it's nec'y to be able to rebroadcast centrally the data that is collected in many places
Raw IP/UDP and IP/TCP isn't a good format for this – fragments, segments, etc
Raw PCAP isn't a good format either
We need messages (NCAP) not packets (PCAP) for this