## Slide 1: Geometry of large networks (computer science perspective)
Dmitri Krioukov (CAIDA/UCSD) AIM, November 2011

## Slide 2: Geometry in computer science
Machine learning and data mining
Bioinformatics
Computer graphics
Distributed systems
Networking

## Slide 3: Geometry of what?
Of the network graph
Of an auxiliary space underlying the graph

## Slide 4: Geometry of what?
Of the network graph
Applications:
  …
Of an auxiliary space underlying the graph
Applications:
  Delay estimation
  Overlay networks
  Routing

## Slide 5: What is the space?
Real
  Geography
  Physical space
Applications
  Geographic routing
  Wireless routing
Hidden / virtual / latent
  Can be virtually anything!
Applications
  Delay estimation
  Overlay routing
  Geometric routing

## Slide 6
Notes: No node has any global knowledge
Congruency is needed (for efficiency, optimality, and robustness)
If congruency is there, shortest paths in network are discrete reflections of smooth shortest (geodesic) paths in the space

## Slide 7: Why routing?
The Internet was designed for and exists to transfer information packets from A to B, where A and B are any two Internet-Protocol- (IP-)talking devices

## Slide 8: IP packet format

## Slide 9: IP addresses
A = 193.137.168.155
B = 192.172.226.78

## Slide 10: IP routes
traceroute 192.172.226.78
1 <1 ms 2 ms 2 ms 193.137.81.254
2 <1 ms <1 ms <1 ms 192.168.255.253
3 1 ms 1 ms 1 ms 193.137.173.254
4 1 ms 1 ms 1 ms 193.136.4.26
5 5 ms 5 ms 5 ms 193.136.1.221
6 5 ms 6 ms 6 ms 193.137.0.30
7 6 ms 6 ms 6 ms 62.40.124.185
8 32 ms 33 ms 32 ms 62.40.112.146
9 41 ms 40 ms 40 ms 62.40.112.137
10 123 ms 124 ms 124 ms 62.40.112.134
11 130 ms 130 ms 129 ms 216.24.184.85
12 134 ms 131 ms 130 ms 216.24.186.23
13 143 ms 144 ms 143 ms 216.24.186.20
14 167 ms 167 ms 167 ms 216.24.186.8
15 199 ms 199 ms 198 ms 216.24.186.30
16 197 ms 197 ms 197 ms 137.164.26.130
17 203 ms 203 ms 203 ms 137.164.25.5
18 204 ms 203 ms 203 ms 137.164.27.50
19 204 ms 205 ms 204 ms 198.17.46.56
20 203 ms 204 ms 204 ms 192.172.226.78

## Slide 11: IP routes
A
B
R1
R3
R4
R2

## Slide 12: Autonomous Systems
Y
X
Z
A

## Slide 13: AS topology
Y
Z
X
A

## Slide 15: Internet AS topology
Cumulative result of local, decentralized, and rather complex interactions between AS pairs
Surprisingly, in 1999, it was found to look completely differently than computer scientists had thought: it shares the two main common features of topologies of other complex networks
  scale-free degree distributions
  strong clustering
Routing protocols have to find and update paths to destinations through it

## Slide 16: IP routing
Intradomain (Interior Gateway Protocols (IGPs))
  routing within an Autonomous System (AS)
  protocols:
    Open Shortest Path First (OSPF)
    Intermediate System to Intermediate System (ISIS)
  Links State (LS) routing protocols
Interdomain (Exterior Gateway Protocols (EGPs))
  routing between Autonomous Systems (ASs)
  protocols:
    Border Gateway Protocol (BGP)
  Path Vector (PV) routing protocol (~Bellman-Ford)

## Slide 17: BGP
Each AS X advertises IP addresses AX that it has
All neighboring ASs receiving this advertisement re-advertise them to their neighbors after pre-pending their AS numbers
The result is that each AS Y has a routing entry for AX which looks like: AX : Y1, Y2, …, X, where Y1 is a neighbor of Y, Y2 is a neighbor of Y1, and so on.

## Slide 18: Simple routing event
Y
X
Z
A
s
t

## Slide 19: BGP dynamics
BGP updates
  2 per second on average
  7000 per second peak rate
Convergence after a single event can take up to tens of minutes

## Slide 20: Compact routing
Memory per node
  Size of the routing tables
Stretch
  How close routing paths are to shortest paths in the network
Communication overhead
  Number of messages the protocol generates per topology change, etc.

## Slide 22: Compact routing overhead
There can be no routing algorithm with the number of messages per topology change scaling better than linearly with the network size in the worst case
Internet-like networks are this worst case
Oops, too bad. Is there anything we can do?

## Slide 23
Notes: In maze without the MAP
Learning its MAP
Dynamic
More complex

## Slide 24
Notes: Direction would be good
Efficiency
Optimality
Robustness
Geometry!!! (no geometry on the previous slide!)
BEST POSSIBLE if all these conditions satisfied

## Slide 25
Notes: No node has any global knowledge
Congruency is needed (for efficiency, optimality, and robustness)
If congruency is there, shortest paths in network are discrete reflections of smooth shortest (geodesic) paths in the space

## Slide 38
Node density
R – disk radius
Node degree
K – disk curvature
Degree distribution
Clustering
maximized

## Slide 42: GR in hyperbolic Internet
Memory per node
  Proportional to its degree
Stretch
  Close to 1 (1.1)
Success ratio
  Close to 1 (0.97)
Communication overhead
  0

## Slide 43: Take-home message


?

## Slide 44: Conclusion
Latent geometry of large complex networks is useful for many applications
For routing, it yields theoretically best possible results (optimal routing), which could not be obtained by any methods for decades
Yet, this research area is
  Quite involved
  Poorly understood
  Only recently attracted some focused attention

## Slide 45
M. Boguñá, F. Papadopoulos, and D. Krioukov, Sustaining the Internet with Hyperbolic Mapping, Nature Communications, v.1, 62, 2010
D. Krioukov, F. Papadopoulos, A. Vahdat, and M. Boguñá, Hyperbolic Geometry of Complex Networks, Physical Review E, v.82, 036106, 2010, Physical Review E, v.80, 035101(R), 2009
F. Papadopoulos, D. Krioukov, M. Boguñá, and A. Vahdat, Greedy Forwarding in (Dynamic) Scale-Free Networks Embedded in Hyperbolic Metric Spaces, INFOCOM 2010, SIGMETRICS MAMA 2009
M. Boguñá, D. Krioukov, and kc claffy, Navigability of Complex Networks, Nature Physics, v.5, p.74-80, 2009